## Slide 1: Leopard Core introduction

## Slide 2: Leopard – e200z4d core
E200z4d processor1
  dual issue hardware architecture
    5 stage of pipeline
  4 Kbyte of instruction cache
  Nexus class 3+ for real time debugging
  supports
    Book E code
      32 bit instruction
    VLE code
      16 bit instruction
  MMU
    16 entries
  Signal processor engine (SPE)
    SIMD instruction
      2 x 32-bit operation simultaneously
      2 x 16-bit operation simultaneously
    DPS instruction
  Floating point unit (FPU)
1) additional details can be found in the training session related to the e200zX

## Slide 3: Block sheme

## Slide 4: Programming Model: e200z4d Register Overview
DEC
DECAR
Decrementer
Auto Reload
TCR
TSR
Control
& Status
TBL
TBU
Time Base
Upper/Lower
Timer Facilities Register Set
SRR0
SRR1
Save & Restore
Registers
ESR
Syndrome
DEAR
Data Exception
Address
IVOR1
l
l
IVOR15
Interrupt Vector
Offset Registers
IVPR
Interrupt
Vector Prefix
CSRR0
CSRR1
Critical S/R
Registers
Interrupt Register Set
MSR
Machine State Register
PVR
Processor Version
PIR
Processor ID
Supervisor Mode Base Register Set
SPR General
Registers
SPRG0
SPRG1
l
l
SPRG9
Storage Control Register Set
PID0
Process Identification Register
SVR
System Version
TLBCFG0
TLBCFG1
MMUCFG
MMU Config
MAS0
l
l
MAS4
MMU Assist
MAS6
Interrupt Vector Offset Registers
HID0
HID1
L1FINV0
Cache Flush
& Invalidate
L1CFG0
Cache Config
L1CSR0
Cache Control
MMUCRS0
MMU Control
and Status
Hardware Implementation
Dependent Registers
e200zX Book E Registers
User Programmer’s Model
SPEFSCR
USPRG0
GPR0
GPR1
GPR31
l
l
l
CR
CTR
LR
XER
DBCNT
Debug Counter
Debug Control
DBCR3-6
Debug Save & Restore
DSRR0
DSRR1
e200zX Specific Registers
DBCR0-2
Debug
Control
IAC1-8
Instruction
Addr. Compare
DBSR
Debug Status
Debug Facilities Register Set
Data Value Compare
DVC2
DVC1
Data Address Compare
DAC2
DAC1
MCSRR0
Machine Check S/R Registers
IVOR32
l
l
IVOR35
L1CFG1
L1CSR1
L1FINV1
MCSRR1
Debug Save & Restore
BTB Control
BUSCR
Notes: Process ID Register (PID, also referred to as PID0). This register is provided to
indicate the current process or task identifier. It is used by the MMU as an extension
to the effective address, and by external Nexus 2/3/4 modules for Ownership Trace
Message generation.
The processor ID register (PIR) contains a value that can be used to distinguish the processor from other processors in the system. The PIR value is read into a GPR using mfspr.
The processor version register (PVR) contains a value identifying the version and revision level of the processor. The PVR distinguishes between processors that differ in attributes that may affect software.
On the e200, the PVR is implemented as defined in Book E. The PVR contents are read into a GPR using mfspr. The PVR is read-only.
Process ID Register (PID, also referred to as PID0). This register is provided to
indicate the current process or task identifier. It is used by the MMU as an extension
to the effective address, and by external Nexus 2/3/4 modules for Ownership Trace

## Slide 5: Instruction timing
Most of instruction executed in a single cycle
  all integer instruction
    except multiply and divide
Branch instruction
  throughput and latency of 2 cycles
  branch prediction can reduce it to 1 cycle
each core embeds 2 execution unit
  dual issue of most instruction

## Slide 6: Cache : Block Diagram
Cache enables faster memory access
Cache is only accessible to the core.
Cache is not accessible to other masters such as:
  eDMA
  FlexRay
Nexus tools can read cache
  when the processor stops
Leopard device includes only Instruction Cache

## Slide 7: MMU: Introduction
All core accesses go through the MMU.
  Memory must be defined in the MMU to be visible to the core
    Otherwise an exception occurs
MMU does not control memory accesses from:
  eDMA
  Flexray
16 entries available
  pages from 1K to 4G
Nexus tools can read MMU settings when the processor stops.
Notes: This presentation will explain these features and how to use them.
The MMU does address translation but you can map logical addresses to physical addresses.
Address translation may be used for the purpose of calibration.
Assembly software must be used to execute the TBL instructions to initialize the MMU. Compiler can not generate the TLB initialization code.
Also MMU provides for memory access timing to allow for external memory emulation during development.

## Slide 8: SPE - Overview
Designed to accelerate DSP operation
  64 bit registers
Single Instruction Multiple Data (SIMD) operation
  2 x 32-bit operation simultaneously
  4 x 16-bit operation simultaneously
Accumulator register
+
+
RA
RB
RD
0
31
32
63

## Slide 9: FPU - Overview
Floating Point unit
  Single precision floating point
Fully IEEE compliant

## Slide 10: Additional details
for additional details refer to the e200zX core training