## Slide 1: LinFlex (UART mode)
Leopard 1M/2M
v.2.0

## Slide 2: LinFlex Overview
LIN Protocol Handler
Standard UART mode
3 operation modes
  Initialization
  Normal
  Sleep
DMA/INTC support
LIN TX
LIN RX
RX/TX
MESSAGE
BUFFER
Filtering Unit
LIN 1.3/2.0/2.1/J2602 Protocol Handler
CONTROL STATUS REGISTERS
Notes: 3 operating modes for power saving and configuration registers lock

## Slide 3: LinFlex UART mode
Full-duplex communication
Selectable frame size:
  8-bit frame
  9-bit frame
  16-bit frame
  17-bit frame
Selectable parity:
  Even
  Odd
  0
  1
4-byte buffer for transmission, 4-byte buffer for reception
12-bit counter for timeout management

## Slide 4: Data frame structure
4 data frame supported
  8 bit data frame
  9 bit data frame
  16 data frame
  17 bit data frame

## Slide 5: Data buffer
8 bytes data buffer
  4 bytes for RX
  4 bytes for TX
Configurable
  Buffer mode
  FIFO mode
    Mandatory when DMA RX/TX is enabled
Notes: In buffer mode the number of data to be sent or received are configured and then written received into the buffer (e.g. to transmit 16bit we write BDR0 and BDR1)
In FIFO mode only BDR0 and BDR4 are visible and the whole buffer is seen as a FIFO

## Slide 6: Timeout (a)
A reception timeout is implemented
  To avoid reception hanging during not expected condition
The timeout counter:
  Starts at zero and counts upward
  Is clocked with the baud rate clock prescaled by a hard-wired scaling factor of 16
  Is automatically enabled when UARTCR[RXEN] = 1
UART preset timeout register contains the preset timeout value
  UARTPTO
UART current timeout register contains the current timeout value in UART mode
  UARTCTO
Notes: Hanging conditions UARTCR[RDFLRFC] is programmed for a certain number of bytes received, but the actual number of bytes received is smaller.

## Slide 7: Timeout (b)
Current value of the timeout counter
  This field is reset whenever one of the following occurs:
    A new value is written to the UARTPTO register
    The value of this field matches the value of UARTPTO[PTO]
    A reset occurs
    New incoming data is received
When timeout expires UARTSR[TO] is set
  CTO matches the value of UARTPTO[PTO]
  An interrupt is generated on Error interrupt line in UART mode
    if enabled by LINIER.DBEIETOIE bit
Notes: Hanging conditions UARTCR[RDFLRFC] is programmed for a certain number of bytes received, but the actual number of bytes received is smaller.
No interrupt are triggered when the timeout expires.
[AR] Interrupt e’ triggerato se abilitato tramite LINIER.DBEIETOIE

## Slide 8: Transmission
Main configuration
  UARTCR[UART] is set
  Set UARTCR[WLx]
    Word length
  Set UARTCR[PCE] Parity control enable
    Set UARTCR[PC] (Parity control (even, odd, 0, 1))
  Set UARTCR[TDFLTFC] field
    number of byte to be transmitted in Buffer mode
    or number the entry in the FIFO
  UARTCR[TXEN] bits set
Transmission starts when BDR0 is programmed
  BDR0 is the least significant byte
After the programmed number of bytes has been transmitted the UARTSR[DTFTFF] flag is set
The buffer can be configured in FIFO mode
  mandatory when DMA Tx is enabled
  UARTCR[TFBM]
Notes: RXEN bit exists to enable the reception
UARTCR[TDFLTFC] pag.1023 of RM rev.9

## Slide 9: Reception (a)
Reception starts as soon as following events occur
  Exits Initialization mode
  Sets the UARTCR[RXEN] field
  Detects the start bit
After the programmed number (RDFL bits) of bytes has been received, the UARTSR[DRFRFE] field is set
The buffer can be configured in FIFO mode
  mandatory when DMA Rx is enabled
  UARTCR[RFBM]

## Slide 10: Reception (a)
Typical reception scenarios
Notes: CLARIFICATION IS NEEDED FOR YOU:In that case, SW needs to take care of timeout by seeing the flag TO or triggering the interrupt. Software has to set the sleep bit to move to idle state

## Slide 11: Reception (b)
Typical reception scenarios
Notes: CLARIFICATION IS NEEDED FOR YOU:In that case, SW needs to take care of timeout by seeing the flag TO or triggering the interrupt. Software has to set the sleep bit to move to idle state

## Slide 12: TX/RX Baud rate
The baud rates set as programmed in the Mantissa (LINIBRR) and Fraction (LINFBRR) registers
  for both receiver and transmitter
LFDIV is an unsigned fixed point
  20 bits for the mantissa (LINIBRR)
  4 bits for the fractional part (LINFBRR)
Example: LFDIV = 25.62
  Mantissa = 25 -> LINIBRR = 25
  Fractional part = 0.62 -> LINFBRR = 10
    0.62 * 2^4 = 9.92 ~10

## Slide 13: Interrupt
Notes: RM pag.1025
Framing error means invalid stop bit

## Slide 14: Interrupt
UARTSR
Timeout interrupt is missing in this table (doc error)
Notes: RM pag.1025
Framing error means invalid stop bit

## Slide 15: DMA
Interface to “connect” 2 DMA channels
  TX fifo
  RX fifo
Notes: Examples in RM ver.9 pag 1055