## Slide 1: ADC
Version 1.0 (PRG)

## Slide 2: ADC Main Features Analog Part
Two independent ADC units with 9 channels each + 4 shared channel
  22 channels in total
Four shared signals for motor control acquisitions
  3 for phase currents
  1 for other acquisitions
1us minimum conversion time (including sample time)
12bit resolution (+/-2LSB)
Sample and Hold separate for each ADC unit
Separate Sampling and Conversion clock prescalers
Single-ended input signal range from 0 to 3.3V (or 5V)
TUE <1.5LSB

## Slide 3: ADC Main Features
Configurable sampling and conversion time duration
Four Analog watchdog channels
Separated conversion result register for each channel
  Right alignment
  Left alignment
Operation Modes
  Normal Mode (One shot / Scan)
  Channel (chain) injection Mode
Driven by
  CPU, or
  CTU
Conversion result overwrite notification
Notes: 4 shared are intended for motor control acquisitions
TUE - total unadjusted error
700ns conversion time is pure conversion time without additional sampling time

## Slide 4: ADC Block schematic

## Slide 5: ADC Normal Conversion Mode 1/2
Normal Conversion Mode is used to convert a single channel or subsequently multiple different channels (a chain)
ADC channels (channel chain) to be converted are selected in Normal Conversion Mask register (NCMR:CH[15:0])
Conversion is started by setting MCR:NSTART bit
Selected channels are subsequently converted and results stored to corresponding data registers (CDRx)
Chain conversion can be stopped by clearing the START bit
Maskable interrupts can be generated (PBR)
  At the End of a single Channel conversion (EOC)
  At the End of the whole channel Chain conversion (ECH)
Notes: CDR includes additional information about the conversion (RM pag.196):
- data is valid?
Previous converted data overwritten before being read
- Result: conversion coming from which kind of conversion (normal, injected or CTU)?

## Slide 6: ADC Normal Conversion Mode 2/2
Normal conversion can be configured in two different modes:
One Shot Mode (MCR:MODE = 0)
  Channels from NCMR are subsequently converted
  After last channel from NCMR is scanned, conversion stops
  Each channel selected in the NCMR chain is converted just once
Scan (continuous) Mode (MCR:MODE = 1)
  Channels from NCMR are subsequently converted
  After the last channel from NCMR is converted, conversion continues, starting from the first channel specified in NCMR again
  Conversion continues until MCR:START bit is cleared

## Slide 7: ADC Injected Conversion Mode 1/2
Injected Conversion Mode is used to suspend ongoing Normal Conversion, convert a new injected chain and resume back the suspended Normal Conversion
Injected chain of channels is specified in Injected Conversion Mask register (JCMR:CH[15:0])
  the same way like previous NCMR
When injected conversion is started (MCR:JSTART):
  Ongoing chain channel conversion is aborted
  Injected chain request is processed – channels specified in NCMR are subsequently scanned (Injected conversion can only be One-shot)
  After last channel from in the injected chain is processed, Normal conversion resumes from the channel at which Normal conversion was aborted

## Slide 8: ADC Injected conversion Mode 2/2
Maskable interrupts can be generated (IMR)
  At the End of a single Injected Channel conversion (JEOC)
  At the End of the whole Injected channel Chain conversion (JECH)
Injected conversion cannot be stopped by clearing MCR:JSTART
Notes: To check: are both JEOC and JECH (or EOX and ECH) generated at the end of the chain?

## Slide 9: ADC Conversion result data format (1)
For each ADC channel the following registers are available:
  Data Register (CDR) to store converted result
Converted result in a Data Register can be either Right or Left aligned (MCR:WLSIDE)
Data overwrite control (MCR:OWREN)
  Overwrite disabled: the new converted results are being discarded until previous DATAREGx value is read
  Overwrite enabled: the new converted result overwrites previous one
Additional conversion information (MCR)
  Overwrite notification
  Conversion mode (Normal / Injected / CTU)
  Is data valid?
Notes: RM pag. 196
CDR includes additional information about the conversion (RM pag.196):
- data is valid?
Previous converted data overwritten before being read
- Result: conversion coming from which kind of conversion (normal, injected or CTU)?

## Slide 10: ADC Interrupts and Flags
All the interrupts share three interrupt lines
The following main flags and maskable interrupts are available to control ADC within application (IMR, WTIMR):
Flag | Description
EOC | End of (a single) channel conversion
ECH | End of (a whole) chain conversion
JEOC | End of (a single) injected channel conversion
JECH | End of (a whole) injected chain conversion
WDGHx, WDGLx | Analog Watchdog Upper, Lower threshold violation
Ref Range | reference voltage is not the expected one (Leopard can work with either 3.3V or 5V)
Self test | Self test fails
Notes: Ref range (RM pad 184) REF RANGE flag

## Slide 11: ADC Conversion Timing
Both sampling and conversion time can be configured separately based on ADC clock
Sampling phase duration (CTR0/1:INPSAMP)
  1-256 ADC clocks
Conversion phase duration (CTR0/1:INPCMP)
Notes: Table in the RM pag.193

## Slide 12: ADC Additional Features: Analog Watchdog
Analog Watchdogs are used to determine whether the ADC converted value lies within guarded area
If the converted value lies outside the guarded area, corresponding threshold violation interrupt can be generated
Each of four Analog Watchdog channels allows to configure
  ADC channel number to be guarded (CWENR0)
  Threshold to be used per channel (CWSEL1/2)
  Upper and lower thresholds (THRHLRn)
  Dedicated interrupt mask for both upper and lower threshold violations events (WTIMR)

## Slide 13: ADC Additional Features: Analog Watchdog

## Slide 14: ADC Additional Features: DMA support
DMA feature is enabled by setting DMAE:DMAEN bit
A DMA access can be programmed after the conversion of every channel by setting the corresponding channel masking bit in DMAR0:DMAx
After channel conversion is finished, ADC generates DMA request (ipd_req)
After DMA controller successfully finishes the transaction, it sets an acknowledge signal (ipd_ack) and ADC releases ipd_req
Notes: ipd_ack could be also released on read form DATAREGx, depending on DMAE:DCLR bit

## Slide 15: ADC Additional Features: Cross Triggering Unit (CTU) support 1/2
CTU can handover ADC control by setting CLR0:CTUEN bit
  From that moment on, CPU (SW) cannot start any conversion
Notes: !!!! To Check !!!!!
    1 DMA request per each CTU FIFO
    DMA generated when all needed samples have been collected

## Slide 16: ADC Additional Features: Cross Triggering Unit (CTU) support 2/2
CTU Mode operation
  CTU set Trigger together with ADC Command (channel number) -> Injected conversion is invoked
  With the last ADC evaluation clocks, the ADC set CTU Next Command signal to demonstrate availability to receive next ADC command
  When the converted result is available, the ADC set CTU Push to signal that CTU Data Out is valid
  CTU can store ADC results in one of four FIFOs; An application can read data from there either by CPU or DMA transfer
Notes: !!!! To Check !!!!!

## Slide 17: ADC Additional Features: Power Down Mode, Auto-clock Off Mode
Power Down Mode (MCR:PWDN)
  In this mode, analog part of ADC is put to low power mode
  No conversion is possible
  Any ongoing chain conversion must be finished (aborted) prior switching to Power Down Mode
Auto-clock off Mode
  A feature enabling to automatically switch off analog clocks (without going to Power Down Mode)
  When enabled, the analog clock is automatically switched off when no any operation is ongoing (ADC is idle)
  MCR:ACKO
Notes: To check: behavior PWDN bit (culd be checked to determine whether ADC is already in pwdn or waked-up?), power-up times, on which power-up time depends
After reset, ADC is in power down by default

## Slide 18: Safety
ADC safety features
  ADC self test
  ADC pre-sampling
  (2 ADCs can be used redundantly)

## Slide 19: Presampling (a)
To detect open failures of the channel multiplexing circuitry
  In addition it allows to discharge the ADC internal capacitor before it starts sampling/conversion of the analog input coming from pads.
    This is useful for resetting information regarding the last converted data.

## Slide 20: Presampling (b)
To detect short failures of the channel multiplexing circuitry

## Slide 21: ADC self test
HW self test
  assisted by SW
Algorithms
  Supply Self test: Algorithm S
    3 conversions
  Resistive-Capacitive Self test: Algorithm RC
    19 conversions
  Capacitive Self test: Algorithm C
    17 conversions
Additional conversion test channel dedicated for Self testing
Flags the error to FCCU in case of failure
Notes: Supply Self test: Algorithm S. It includes the conversion of the ADC internal bandgap voltage, ADC supply voltage, and ADC reference voltage. It includes a sequence of 3
test conversions (steps). The supply test conversions must be an atomic operation (no functional conversions interleaved).
Resistive-Capacitive Self test: Algorithm RC. It includes a sequence of 19 test conversions (steps) by setting the ADC internal resistive digital-to-analog converter (DAC).
Capacitive Self test: Algorithm C. It includes a sequence of 17 test conversions (steps) by setting the capacitive elements comprising the sampling capacitor/ capacitive DAC.

## Slide 22: ADC self test
Driven by
  CTU
  CPU
CPU
  One shoot mode
    A single selt test conversion is executed
    The step number and algorithm to be executed is programmed in STCR3 register
  Scan mode
    consecutive steps self test algorithm are converted continuously at the end of each chain of normal conversions
Notes: MCR[MODE] = 1
Examples pag.224 of the RM
CTU
The RC and C algorithm can be executed, programming the CLRx registers, in one of the following schemes:

## Slide 23: ADC self test
Driven by
  CTU
  CPU
CTU
  Algorithm S
    atomic
  Algorithm C and RC
    Burst
      when the CTU schedules the execution of the CLRx register configured for the self testing, both the algorithms RC and C are executed in burst mode
    Interlived
      when the CTU schedules the execution of the CLRx register configured for the self testing, a single step of the algorithm RC or C is executed according to an internal counter.
      In this mode the ADC self testing procedure is distributed and the functional conversions are not stalled for a long time.
Notes: MCR[MODE] = 1
Examples pag.224 of the RM
CTU
The RC and C algorithm can be executed, programming the CLRx registers, in one of the following schemes:
(step0- algRC, step1-algRC, ...stepN-algRC, step0-algC, step1-algC, ... stepM-algC).
Command list (RM 307)

## Slide 24
Thanks for you Attendance! – Q & A