## Slide 1: Periodical Interrupt Timer
Version 1.0

## Slide 2: PIT Timer Module
4 general purpose interrupt timers
32-bit counter resolution
  downcounter
Each Timer can generate periodic
  DMA transfer
  interrupts
All interrupts/DMA transfer are maskable
Independent timeout periods for each timer
Notes: 4 timers share the same register interface
they trigger different interrupt/DMA request

## Slide 3: PIT Timer Module: Timers 1/2
The timers generate triggers at periodic intervals, when enabled.
  LDVAL registers contain start values
  Count down until they reach 0.
  Start value is loaded again
  Each time a timer reaches 0, it will generate a trigger pulse, and set the interrupt flag.
  All interrupts can be enabled or masked (by setting the TIE bits in the TCTRL registers).
  A new interrupt can be generated only after the previous one is cleared.
Notes: This slide shows the functionality of the PIT
Trigger means either interrupt or DMA transfer request.

## Slide 4: PIT Timer Module: Timers 2/2
If desired, the current counter value of the timer can be read via the CVAL registers.
  The counter value can be restarted/changed,
    by first disabling
    (setting a new load value)
    then enabling the timer with the TEN bit
  The counter period can be changed without restarting the timer by writing the LDVAL register with the new load value.
    This value will then be loaded after the next trigger event

## Slide 5: PIT Timer Module
4 general purpose interrupt timers
32-bit counter resolution
  downcounter
Each Timer can generate periodic
  DMA transfer
  interrupts
All interrupts/DMA transfer are maskable
Independent timeout periods for each timer

## Slide 6: PIT Timer Module: Example
Configuration:
  the PIT clock has a frequency of 50 MHz
  timer 1 shall create an interrupt every 5.12 ms
  timer 3 shall create a trigger event every 30 ms
First the PIT module needs to be activated by writing a 0 to the MDIS bit in the PITCTRL register.
The 50 MHz clock frequency equates to a clock period of 20 ns . Timer 1 needs to trigger every 5.12 ms/20
ns = 256000 cycles and timer 3 every 30 ms/20 ns = 1500000 cycles. The value for the LDVAL register trigger would be calculated as (period / clock period) -1.
This means that LDVAL1 with 0003E7FF hex and LDVAL3 with 0016E35F hex.
The interrupt for Timer 1 is enabled by setting TIE in the TCTRL1 register.
The timer is started by writing a 1 to bit TEN in the TCTRL1 register.
Timer 3 shall be used only for triggering. Therefore Timer 3 is started by writing a 1 to bit TEN in the TCTRL3 register, bit TIE stays at 0.