## Slide 1: System timer module
Version 1.0

## Slide 2: STM Overview
The System Timer Module (STM) is a 32-bit timer designed to support commonly required system and application software timing functions.
STM has the following features:
  One 32-bit up counter with 8-bit pre-scaler
  Four 32-bit compare channels
  Independent interrupt source for each compare
  Counter can be stopped in debug mode
STM supports two device modes of operation:
  Normal (its counter runs continuously)
  Debug (operation of the counter is controlled by the FRZ bit in the STM_CR register)

## Slide 3: STM Functional description 1/2
STM has one 32-bit up counter (STM_CNT) that is used as the time base for all channels
Counter increments at the system clock frequency divided by a pre-scaler value (STM_CR[CPS] field
  any value in the range from 1 to 256
Counter is enabled with the STM_CR[TEN] bit.
  normal mode the counter continuously increments.
  debug mode the counter operation is controlled by the STM_CR[FRZ] bit.
Counter rolls over at 0xFFFF_FFFF to 0x0000_0000 with no restrictions at this boundary

## Slide 4: STM Functional description 2/2
STM has four compare channels, configured by:
  a channel control register (STM_CCRn),
  a channel interrupt register (STM_CIRn)
  a channel compare register (STM_CMPn).
Channel is enabled by setting the STM_CCRn[CEN] bit.
Channel will set the STM_CIR[CIF] bit (when enabled) and generate an interrupt request when the channel compare register matches the timer counter.
The interrupt request is cleared by writing a 1 to the STM_CIRn[CIF] bit.
STM counter does not count when the system clock is stopped